## Slide 1: A Mathematical Formulation of Cost-Aware Buffer Placement for Dataflow Circuit Optimization
Yuan Qin
July 16th, 2024

## Slide 2
Background
HLS: codes to circuits
Dynamic HLS produces high performance dataflow circuits
This work: A strategy to reduce the cost of HLS-produced dataflow circuits
Merge
Branch
Load A[i]
+
Fork
1
Fork
<
900
Start: i=0
Load B[i]
Store A[i]
+
for (i=0; i<900; i++)
A[i] = A[i] + B[i];
Handshake Mechanism
Merge
Fork
Valid
Ready
Data
Ready
Valid
Data

## Slide 3
Background
Optimizing dataflow circuit performance  optimizing loops (CFDFCs)
Merge
Branch
Load A[i]
+
Fork
1
Fork
<
900
Start: i=0
Load B[i]
Store A[i]
+
Merge
Branch
Require a Choice

## Slide 4
Background
Optimizing dataflow circuit performance  optimizing loops (CFDFCs)
Merge
Branch
Load A[i]
+
Fork
1
Fork
<
900
Start: i=0
Load B[i]
Store A[i]
+
Join
Fork
Do not require a Choice

## Slide 5
Background
Optimizing dataflow circuit performance  optimizing loops (CFDFCs)
Merge
Branch
Load A[i]
+
Fork
1
Fork
<
900
Start: i=0
Load B[i]
Store A[i]
+
900 Times
Choice-free Dataflow Circuit
(CFDFC)
Load A[i]
+
Fork
1
Fork
<
900
Load B[i]
Store A[i]
+
Join
for (i=0; i<900; i++)
A[i] = A[i] + B[i];

## Slide 6
Background
Choice-free Dataflow Circuit
(CFDFC)
Load A[i]
+
Fork
1
Fork
<
900
Load B[i]
Store A[i]
+
Join

## Slide 7
Why Buffer Placement is Important?
reg
🤝
Buffers
Regulate critical paths
Accommodate tokens
Help improve throughput
(Requires a good placement)
Next slide: example of suboptimal placement leads to throughput degradation
Choice-free Dataflow Circuit
(CFDFC)
Load A[i]
+
Fork
1
Fork
<
900
Load B[i]
Store A[i]
+
Join

## Slide 8
Fork
*
+
Stall
*
+
BUFF
Fork
Assume Initiation Interval (II) = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
+
*

## Slide 9
Fork
Stall
BUFF
Fork
Assume Initiation Interval (II) = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
II = 5
+
*
+
*

## Slide 10
Fork
*
Stall
*
Fork
Assume Initiation Interval (II) = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
II = 5
+
+

## Slide 11
Fork
*
Stall
*
Fork
Assume Initiation Interval (II) = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
II = 5
+
+

## Slide 12
Fork
*
Stall
*
Fork
Assume Initiation Interval (II) = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
II = 5
+
+

## Slide 13
Fork
*
Stall
*
Fork
Assume Initiation Interval (II) = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
II = 5
+
+

## Slide 14
Fork
*
Stall
*
Fork
Assume Initiation Interval (II) = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
II = 5
+
+

## Slide 15
Fork
*
Stall
*
Fork
Assume Initiation Interval (II) = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
II = 5
+
+

## Slide 16
Fork
*
Stall
*
Fork
Assume Initiation Interval (II) = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
II = 5
+
+

## Slide 17
Fork
*
Stall
*
Fork
Assume Initiation Interval (II) = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
II = 5
II = 1
+
+

## Slide 18
Fork
*
Stall
*
BUFF
Fork
Assume Initiation Interval = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
Fork
(Sender)
*
(Receiver)
+
+
Notes: Let’s imagine a token is valid on the sender side,……….(替代only one token）

## Slide 19
Fork
*
Stall
*
BUFF
Fork
Assume Initiation Interval = 1
Why Buffer Placement is Important?
Can these circuits take token every II=1 cycle?
Fork
(Sender)
*
(Receiver)
BUFF
+
+

## Slide 20
We Have Achieved the Best Throughput, But Can We Do Better?
Fork
*
Stall
*
BUFF
Fork
LUT # = 81
Register # = 168
(Under bitwidth 32)
Slot # = 5
Transparent FIFO
Buffers occupy the majority of the circuit area: we should place them strategically
+
+
Notes: The transparent fifo is very expensive but it is not the only buffer to achieve the best throughput

## Slide 21
Can We Use Cheaper Buffers While Maintaining the Throughput?
*
BUFF
Fork
LUT # = 81
Register # = 168
Transparent FIFO
LUT # = 10
Register # = 165
OEHB Chain
A wider range of buffer types
LUT # = 1
Register # = 165
Pipeline
Buffers occupy the majority of the circuit area: we should place them strategically
+
Head
Tail
Notes: 标上head and tail

## Slide 22
Motivation
*
FIFO
Fork
Transparent FIFO
OEHB Chain
A wider range of buffer types
Pipeline
LUT # = 81
Register # = 168
LUT # = 10
Register # = 165
LUT # = 1
Register # = 165
Buffers occupy the majority of the circuit area: we should place them strategically
+
Head
Tail

## Slide 23
Motivation
*
FIFO
Fork
Transparent FIFO
OEHB Chain
A wider range of buffer types
Pipeline
LUT # = 81
Register # = 168
LUT # = 10
Register # = 165
LUT # = 1
Register # = 165
Buffers occupy the majority of the circuit area: we should place them strategically
+
Head
Tail

## Slide 24
Motivation
*
FIFO
Fork
Transparent FIFO
OEHB Chain
A wider range of buffer types
Pipeline
LUT # = 81
Register # = 168
LUT # = 10
Register # = 165
LUT # = 1
Register # = 165
Buffers occupy the majority of the circuit area: we should place them strategically
+
Head
Tail

## Slide 25
Motivation
*
FIFO
Fork
Transparent FIFO
OEHB Chain
A wider range of buffer types
Pipeline
LUT # = 81
Register # = 168
LUT # = 10
Register # = 165
LUT # = 1
Register # = 165
Buffers occupy the majority of the circuit area: we should place them strategically
+
Head
Tail

## Slide 26
Motivation
*
FIFO
Fork
Transparent FIFO
OEHB Chain
A wider range of buffer types
Pipeline
LUT # = 81
Register # = 168
LUT # = 10
Register # = 165
LUT # = 1
Register # = 165
Buffers occupy the majority of the circuit area: we should place them strategically
+
Head
Tail

## Slide 27
Motivation
*
FIFO
Fork
Transparent FIFO
OEHB Chain
A wider range of buffer types
Pipeline
LUT # = 81
Register # = 168
LUT # = 10
Register # = 165
LUT # = 1
Register # = 165
Buffers occupy the majority of the circuit area: we should place them strategically
+
Head
Tail
Notes: 记得提及all valid

## Slide 28
Motivation
*
FIFO
Fork
Transparent FIFO
OEHB Chain
A wider range of buffer types
Pipeline
Same performance, but very different costs!
LUT # = 81
Register # = 168
LUT # = 10
Register # = 165
LUT # = 1
Register # = 165
+
Head
Tail

## Slide 29
Motivation
*
FIFO
Fork
Transparent FIFO
OEHB Chain
A wider range of buffer types
Pipeline
Our work: Automatically selects the cheapest solution while maintaining the performance
LUT # = 81
Register # = 168
LUT # = 10
Register # = 165
LUT # = 1
Register # = 165
+
Head
Tail

## Slide 30
Prior Works Cannot Achieve This
Limitations of the prior works:
Ignoring the cost differences between buffer types
Only two buffer types

## Slide 31
Our Contribution: A New Buffer Placement Strategy
Objectives: Minimizing area cost, maximizing throughput.
How? A general cost + performance model for buffers.
What are the attributes of these buffers?
Notes: Model--》attribute glue text

## Slide 32
We Model the Buffers in This Way
Minimum latency
Maximum latency
Slot number
N-slots
Decompose N-slot to 1-slot
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
……
In the following: We study the single-slot properties of these buffer types
Notes: 提一下标题;
We will see what these attributes mean specifically in the following examples

## Slide 33
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
Min. latency =
Max. latency =
Cycle 0
We Model the Buffers in This Way
Minimum latency means the minumum clock cycles a token resides in this buffer during the whole process it passes through the buffer.
Maximum latency means the maximum clock cycles a token resides in this buffer which will not violate the initiation interval of the circuit.
Notes: 把定义打在上面并留到整个过程

## Slide 34
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
Min. latency =
1
Cycle 0
Cycle 1
Max. latency =
We Model the Buffers in This Way
Minimum latency means the minumum clock cycles a token resides in this buffer during the whole process it passes through the buffer.
Maximum latency means the maximum clock cycles a token resides in this buffer which will not violate the initiation interval of the circuit.

## Slide 35
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
Buffer incapable of storing a certain max. latency  system stall
Min. latency =
Cycle 0
Max. latency =
1
We Model the Buffers in This Way
Minimum latency means the minumum clock cycles a token resides in this buffer during the whole process it passes through the buffer.
Maximum latency means the maximum clock cycles a token resides in this buffer which will not violate the initiation interval of the circuit.

## Slide 36
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
Buffer incapable of storing a certain max. latency  system stall
Min. latency =
Cycle II
Max. latency =
1
We Model the Buffers in This Way
Minimum latency means the minumum clock cycles a token resides in this buffer during the whole process it passes through the buffer.
Maximum latency means the maximum clock cycles a token resides in this buffer which will not violate the initiation interval of the circuit.

## Slide 37
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
Buffer incapable of storing a certain max. latency  system stall
Min. latency =
Cycle II
Max. latency =
Cycle II
1
II
We Model the Buffers in This Way
Minimum latency means the minumum clock cycles a token resides in this buffer during the whole process it passes through the buffer.
Maximum latency means the maximum clock cycles a token resides in this buffer which will not violate the initiation interval of the circuit.

## Slide 38
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
N-slots
Min. latency = N
Max. latency = N * II
We Model the Buffers in This Way
Minimum latency means the minumum clock cycles a token resides in this buffer during the whole process it passes through the buffer.
Maximum latency means the maximum clock cycles a token resides in this buffer which will not violate the initiation interval of the circuit.

## Slide 39
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
Min. latency =
Max. latency =
0
Cycle 0
We Model the Buffers in This Way
Minimum latency means the minumum clock cycles a token resides in this buffer during the whole process it passes through the buffer.
Maximum latency means the maximum clock cycles a token resides in this buffer which will not violate the initiation interval of the circuit.
Notes: 在slot上面加bypass
把network去掉

## Slide 40
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
Min. latency =
Max. latency =
0
II - 1
Buffer incapable of storing a certain max. latency  system stall
Cycle II
Cycle II-1
We Model the Buffers in This Way
Minimum latency means the minumum clock cycles a token resides in this buffer during the whole process it passes through the buffer.
Maximum latency means the maximum clock cycles a token resides in this buffer which will not violate the initiation interval of the circuit.

## Slide 41
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
N-slots
Min. latency = 0
Max. latency = N * (II – 1)
We Model the Buffers in This Way
Minimum latency means the minumum clock cycles a token resides in this buffer during the whole process it passes through the buffer.
Maximum latency means the maximum clock cycles a token resides in this buffer which will not violate the initiation interval of the circuit.

## Slide 42
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
Min. latency = 0
Max. latency = N * II
We Model the Buffers in This Way
Minimum latency means the minumum clock cycles a token resides in this buffer during the whole process it passes through the buffer.
Maximum latency means the maximum clock cycles a token resides in this buffer which will not violate the initiation interval of the circuit.
N-slots

## Slide 43
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
🤝
Not ready!
Min. latency = N
Max. latency =
Min. latency =
Max. latency =
We Model the Buffers in This Way
Minimum latency means the minumum clock cycles a token resides in this buffer during the whole process it passes through the buffer.
Maximum latency means the maximum clock cycles a token resides in this buffer which will not violate the initiation interval of the circuit.
N-slots

## Slide 44
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
In summary, the relationship between
buffer type, slot number, latency, and circuit II
We Model the Buffers in This Way
In the next, we should integrate our model into prior works
Notes: 后面说，in the next we should Integrate our model into prior works

## Slide 45
Integrate Our Buffer Model into the Prior Works
1/3
1/3
1/3
2/3
Latency  Token occupancy
Little’s law:
Prior Works: the relationship between
buffer type, slot number, token occupancy, and circuit throughput
Notes: buffer type, slot number, token occupancy, and circuit II

## Slide 46
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
Integrate Our Buffer Model into the Prior Works

## Slide 47
Optimization Model
Timing Constraints
Throughput Constraints
Mixed Integer Quadratically Constrained Programming (MIQCP)
Objective
Notes: 把constraints放进一页

## Slide 48
Optimization Model
Objective:
OEHB Chain
Full-tran. FIFO
TEHB Chain
Pipeline
2
25
19
<1
Not linear in fact!
Weighted sum of all CFDFCs’ throughput the total buffer area
Buffer area is a function of slot number
Gain coefficients by synthesis (LUT #)
Notes: 文本的方式去写，we maximize throughput minimize buffer cost

## Slide 49
Experimental Results
We experimented on 9 benchmarks where we perform buffer placement strategy of dynamitic, our work and FPGA ’20 (using gurobi). The target clock period is 6ns.
We run Modelsim to calculate total clock cycles (representing throughput) and run Vivado synthesis to calculate area cost.
We mainly compare LUT costs, and make sure our work achieves the best throughput. Register costs and timing slack should be within a reasonable range.

## Slide 50
Experimental Results
Benchmark | Cycle # |  |  | Slack |  | 
 | Dynamatic | Our Work | FPGA20 | Dynamatic | Our Work | FPGA20
fir | 1014 | 1014 | 1014 | 2.084 | 1.324 | 1.313
iir | 5007 | 4008 | 4008 | 1.066 | 2.267 | 1.964
if_loop_1 | 213 | 113 | 112 | 0.617 | 0.462 | 0.518
if_loop_2 | 211 | 111 | 111 | 0.619 | 0.521 | 0.451
sumi3_mem | 1019 | 1018 | 1018 | 2.041 | 2.268 | 2.278
vedio_filter | 1368 | 949 | 948 | 0.856 | 0.957 | 0.893
matvec | 10119 | 10119 | 10118 | 1.551 | 0.272 | 0.471
image_resize | 1065 | 945 | 944 | 1.789 | 1.997 | 0.99
matrix | 40548 | 27948 | 27948 | 1.187 | 0.975 | 0.779
Notes: 目标放到slides上，下面放结论
Fpga20改进了dynamatic的implementation，把不对的东西纠正了，为了对比也放在上面。
单独一页详细说比较的东西。

## Slide 51
Experimental Results
Benchmark | Utilization |  |  |  |  |  |  |  |  | Savings (%) Compared with |  |  | 
 | Dynamatic |  |  | Our work |  |  | FPGA '20 |  |  | FPGA '20 |  | Dynamatic | 
 | LUT |  | Register | LUT |  | Register | LUT |  | Register | LUT | Reg. | LUT | Reg.
 | Total | Logic |  | Total | Logic |  | Total | Logic |  |  |  |  | 
fir | 466 | 470 | 531 | 436 | 434 | 528 | 461 | 457 | 535 | 5.4 | 1.3 | 6.44 | 0.56
iir | 666 | 666 | 869 | 700 | 689 | 844 | 826 | 810 | 848 | 15.3 | 0.5 | -5.11 | 2.88
if_loop_1 | 521 | 521 | 630 | 594 | 592 | 668 | 664 | 660 | 736 | 10.5 | 9.2 | -14.01 | -6.03
if_loop_2 | 543 | 543 | 596 | 602 | 602 | 629 | 625 | 625 | 666 | 3.7 | 5.6 | -10.87 | -5.54
sumi3_mem | 437 | 409 | 426 | 373 | 339 | 469 | 435 | 407 | 457 | 14.3 | -2.6 | 14.65 | -10.09
vedio_filter | 1547 | 1459 | 1187 | 1326 | 1247 | 1322 | 1593 | 1485 | 1400 | 16.8 | 5.6 | 14.29 | -11.37
matvec | 699 | 641 | 579 | 575 | 533 | 597 | 673 | 653 | 604 | 14.6 | 1.2 | 17.74 | -3.11
image_resize | 612 | 564 | 531 | 595 | 551 | 562 | 646 | 606 | 630 | 7.9 | 10.8 | 2.78 | -5.84
matrix | 841 | 777 | 587 | 656 | 642 | 599 | 774 | 754 | 639 | 15.2 | 6.3 | 22.00 | -2.04

## Slide 52
Experimental Results
Benchmark | Total Slot # |  |  |  |  |  |  |  | LUT Reduction
 | Our Work |  |  |  | FPGA '20 |  |  |  | 
 | OEHB | TEHB | FIFO | Pipeline | OEHB | TEHB | FIFO | Pipeline | 
fir | 3 | 3 | 0 | 9 | 3 | 3 | 9 | 0 | 25
iir | 5 | 5 | 0 | 5 | 6 | 6 | 2 | 0 | 126
if_loop_1 | 6 | 4 | 0 | 6 | 7 | 7 | 4 | 0 | 70
if_loop_2 | 7 | 4 | 0 | 0 | 7 | 7 | 0 | 0 | 23
sumi3_mem | 3 | 3 | 0 | 20 | 3 | 3 | 20 | 0 | 62
vedio_filter | 9 | 5 | 0 | 53 | 10 | 10 | 49 | 0 | 267
matvec | 8 | 4 | 0 | 26 | 9 | 9 | 19 | 0 | 98
image_resize | 8 | 4 | 0 | 13 | 9 | 9 | 10 | 0 | 51
matrix | 13 | 5 | 0 | 26 | 13 | 13 | 23 | 0 | 118

## Slide 53
An Interesting Finding
TEHB
OEHB
OEHB
TEHB
LUT #: 494
LUT #: 436
In fir

## Slide 54
Limitations and Future Work
Lazy fork vs. eager fork
Synthesize buffer alone vs. whole circuit
Not linear area utilization
Long runtime
Variable units

## Slide 55
Q&A

## Slide 56
Motivation
*
*
FIFO
Fork
Transparent FIFO
OEHB Chain
If the channel is on another CFDFC where:
Pipeline
Lat.=3
LUT # = 81
Register # = 168
LUT # = 10
Register # = 165
LUT # = 1
Register # = 165

## Slide 57
Motivation
*
*
FIFO
Fork
Slot # = 5
Transparent FIFO
Slot # = 5
OEHB Chain
If the channel is on another CFDFC where:
Slot # = 5
Pipeline
Valid
Valid
Not Valid!
Not Valid!
Stall
Stall
Back pressure!
Throughput ↓

## Slide 58
Optimization Model
Timing constraints for the whole circuit.

## Slide 59
Attributes of Buffers
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
Min./Max latency under a specific II of CFDFC
#1~II
*
*
Fork
#0
#II+1~2*II
#1~II
#II+1~2*II
#>2*II
#1~II
Min. latency = 0
#II+1
#II+1
1
0
0
x
Max. latency = II-1

## Slide 60
Integrate Our Buffer Model into the Prior Works
FPGA ’20
Buffers
Our model
CDFG
Notes: 介绍一下prior是干什么的，解出来每个channel上的token occupancy；列出模型constraints强调只要小改动就能让他工作，包括objective也放在一起，一页。

## Slide 61
Integrate Our Buffer Model into the Prior Works
V
D
R
Notes: 介绍一下prior是干什么的，解出来每个channel上的token occupancy；列出模型constraints强调只要小改动就能让他工作，包括objective也放在一起，一页。

## Slide 62
Integrate Our Buffer Model into the Prior Works
FPGA ’20
Buffers
Our model
CDFG
Notes: 介绍一下prior是干什么的，解出来每个channel上的token occupancy；列出模型constraints强调只要小改动就能让他工作，包括objective也放在一起，一页。

## Slide 63
Integrate Our Buffer Model into the Prior Works
FPGA ’20
Buffers
Our model
CDFG
Channels’ token occupancies decide throughput
Notes: 介绍一下prior是干什么的，解出来每个channel上的token occupancy；列出模型constraints强调只要小改动就能让他工作，包括objective也放在一起，一页。

## Slide 64
Optimization Model
Throughput constraints for each CFDFC.
OEHB Chain
TEHB Chain
Full-transparent FIFO
Pipeline
Each channel can have mixed types of buffer.
Mixed Integer Quadratically Constrained Programming (MIQCP)
Notes: 把constraints放进一页

## Slide 65
Back up
TEHB 642
OEHB 643
Pipeline 653
LUT #:
Notes: 把constraints放进一页

## Slide 66
Back up
Benchmark | Utilization |  |  |  |  |  |  |  |  | Savings (%) Compared with |  |  | 
 | Dynamatic |  |  | Our work |  |  | FPGA '20 |  |  | Dynamatic |  | FPGA '20 | 
 | LUT |  | Register | LUT |  | Register | LUT |  | Register | LUT | Reg. | LUT | Reg.
 | Total | Logic |  | Total | Logic |  | Total | Logic |  |  |  |  | 
fir | 466 | 470 | 531 | 415 | 413 | 483 | 461 | 457 | 535 | 10.0 | 9.7 | 10.94 | 9.04
iir | 666 | 666 | 869 | 622 | 611 | 764 | 715 | 715 | 946 | 13.0 | 19.2 | 6.61 | 12.08
if_loop_1 | 521 | 521 | 630 | 523 | 521 | 568 | 626 | 622 | 702 | 16.5 | 19.1 | -0.38 | 9.84
if_loop_2 | 543 | 543 | 596 | 524 | 524 | 529 | 594 | 594 | 631 | 11.8 | 16.2 | 3.50 | 11.24
sumi3_mem | 437 | 409 | 426 | 372 | 338 | 422 | 435 | 407 | 457 | 14.5 | 7.7 | 14.87 | 0.94
vedio_filter | 1547 | 1459 | 1187 | 1227 | 1148 | 1255 | 1569 | 1473 | 1325 | 21.8 | 5.3 | 20.69 | -5.73
matvec | 699 | 641 | 579 | 522 | 504 | 521 | 633 | 605 | 595 | 17.5 | 12.4 | 25.32 | 10.02
image_resize | 612 | 564 | 531 | 509 | 465 | 514 | 622 | 582 | 588 | 18.2 | 12.6 | 16.83 | 3.20
matrix | 841 | 777 | 587 | 628 | 614 | 541 | 722 | 710 | 607 | 13.0 | 10.9 | 25.33 | 7.84
No ready path delay. Throughput unchanged
Notes: 把constraints放进一页

## Slide 67
Interesting Findings
OEHB
TEHB
OEHB
TEHB
LUT #: 494
LUT #: 436
In fir
Elastic Buffer